## “When to do a STLC extraction”

The limits for STLC and TTLC metals are listed below along with the range of TTLC concentrations for which a STLC extraction must be done.

| SUBSTANCE | STLC (mg/L) | RANGE OF TTLC VALUES FOR WHICH AN STLC MUST BE DONE | TTLC (mg/kg) |
| --- | --- | --- | --- |
| Antimony | 15 | 150 mg/kg or greater | 500 |
| Arsenic | 5.0 | 50 mg/kg or greater | 500 |
| Barium | 100 | 1000 mg/kg or greater | 10,000 |
| Beryllium | 0.75 | 7.5 mg/kg or greater | 75 |
| Cadmium | 1.0 | 10 mg/kg or greater | 100 |
| Chromium 6 | 5.0 | 50 mg/kg or greater | 500 |
| Chromium | 5.0 | 50 mg/kg or greater | 2,500 |
| Cobalt | 80 | 800 mg/kg or greater | 8,000 |
| Copper | 25 | 250 mg/kg or greater | 2,500 |
| Lead | 5.0 | 50 mg/kg or greater | 1,000 |
| Mercury | 0.2 | 2 mg/kg or greater | 20 |
| Molybdenum | 350 | 3,500 mg/kg or greater | 3,500 |
| Nickel | 20 | 200 mg/kg or greater | 2,000 |
| Selenium | 1.0 | 10 mg/kg or greater | 100 |
| Silver | 5.0 | 50 mg/kg or greater | 500 |
| Thallium | 7.0 | 70 mg/kg or greater | 700 |
| Vanadium | 24 | 240 mg/kg or greater | 2,400 |
| Zinc | 250 | 2,500 mg/kg or greater | 5,000 |

If you have a solid sample analyzed for metals (TTLC) you must do an STLC for those metals that are 10 times or greater than the STLC limit. For example – The TTLC limit for antimony is 500 mg/kg and the STLC limit is 15 mg/L. If your TTLC result is 150 mg/kg or higher they you must do an STLC for antimony.